## Slide 1: Solubility Curve Lab

## Slide 2: Teacher
- Turn on room fan
- Remind them not to reach OVER a flame
- Set a timer to press Stops & turn off the fan

## Slide 3: Alter lab in following way (groups of 3-4)
Use a gentle BLUE flame (orange will result in black t.t.)
Need an empty larger Beaker to have a spot to put t.t. down or large t.t. Holder
Be MOVING flame slowly underneath for even heating
Angle away from classmates
Only heat until all is dissolved (NOT 90C) the first time
Turn of the Bunsen burner at this point
Use a coloured paper behind t.t. to watch for crystals
If you are fast at adding water, it will all re-dissolve WITHOUT further heating.
TASKS TO DIVIDE: holding test tube, watching for crystals, recording temperature, adding more water
Final few data points:
You can hold the test tube intermittently to get the temperature to lower faster.
If time allows you could also place the tube in cold or ice water

## Slide 4: IN LAB - GROUPS OF 4
PRACTICE with bulbs and pipettes first if needed
Draw up 3 or more ml of water, remove tip from water and remove bulb, covering end with finger and releasing until exactly 2 ml. Do this IN ADVANCE so can quickly add it to test tube
TASKS: holding test tube, watching for crystals, recording temperature, adding more water
Need TWO beakers -> one of distilled water to ADD and empty one to hold test tube as needed.
Clean up:
- Dispose of liquid in provided beaker - Wash test tubes with a scrub brush in sink with soapy water
- Wash all other glassware and return to where you got it, ensure all beakers are cleaned etc.

## Slide 5: Equipment list
Ammonium chloride small beakers with scoopulas
Retort stands
Thermometers
Tt clamps (and pinchers)
Hot mits
10 ml pipettes & bulb, 10 ml cylinders & droppers, FYI Plastic pipette bulbs have a 2 ml marking so can also be used.
Large & wide tt
Enough beakers for distilled water and a holder
Test tube holders